## Slide 1: EE-466:Power System Protection
Your Complete Name Here:

## Slide 2: Basic Introduction:
In this Project, We are asked to design a Protection Scheme for a Power System.
For Protection, we add Circuit Breakers in front of every component. Then we add Current Transformer (CT’s) for Proper measuring of current. Then we add Relays to trip Circuit Breaker at the time of Fault.

## Slide 3: Power System Introduction:
Basically this power system has contains:
Sr No. | Components | Quantity
1 | Power Grid | 1
2 | Transformers | 6 (All Step Down)
3 | Lump Load | 1
4 | Static Load | 2
5 | Generator | 1
6 | Synchronous Motor | 1
7 | Induction Motor | 5

## Slide 4: Configurations:
We are asked to Design Protection Scheme for TWO Configuration:
Closed Tie Configuration:
In this Configuration, All Circuit Breakers are closed.
Opened-tie CB-1 Configuration:
In this Configuration, All Circuit Breakers are closed But CB-1 is Open(which connects BUS5 and BUS6).
Now, let’s discuss the Procedure…

## Slide 5: Procedure:
First we make the Complete Power System on ETAP.
After making the system we run Load Flow Analysis to see the IMAX-LOAD.
Then we run Short Circuit Analysis to see Ifault.
Then we add Current Transformer in front of every component. The CT’s rating should be set on the IMAX-LOAD Flowing through each component.
Then we set relay’s. For Proper Relay Setting we need IPICKUP this can be find through
2 x IMax-Load < IPickup < 1/3 x IMIN-Fault
In ETAP, if we enter Pickup value in relay settings then it automatically displays IPickup. So, we randomly entered some values for Pickup to get Desired IPickup for every component. By this Process we got Pickup value for Every Component. And by this Process we set All Relays.
Then we insert Fault one by one on every BUS to test Our PROTECTION SCHEME and to see the Tripping Sequence of Circuit Breakers & Relays.

## Slide 6: Then, we repeat All the Steps For 2nd Configuration i.e., Opened-tie CB-1 All the Figures, Tables & Relay Sequence of Operation is mentioned in Project Report

## Slide 7: Conclusion & Results:
The Project was about designing a Protective Scheme for a given Diagram.
Load Flow Analysis results help us to choose CT Ratios.
In Opened-tie Configuration, in some faults (like BUS 5 , BUS 6) are simpler to handle. This is due to the Isolation of elements between the two parts of Diagram.
It was a very interesting Project and it enhanced our understanding of the course especially in relay coordination.

## Slide 8: Thank You So MUCH ! For Your Attention.